## Slide 1
VPI Signal and Fan-In Tracer
A technical deep dive into how the tracer reconstructs a signal’s driver cone live inside Xcelium — no waveform database.
SETUP AT START · RECORD DURING RUN · REPORT AT END
Notes: Open on the mission, not the code. The tool answers one question live, inside the simulator, with no waveform database. Everything in the deck serves that single question.

## Slide 2
PROJECT OVERVIEW
The One Question We Answer
“For one signal at one moment in a simulation, what drove it, with what value, from which source line?”
That backward dependency set is the signal’s fan-in cone.
One self-contained VPI shared library, loaded into Xcelium with -loadvpi.
It walks the design, records activity, and writes trace_output.json plus an interactive HTML report.
FAN-IN CONE OF q
clk
d
1'b0
DFF
q
clock
data
const
The trace walks BACKWARD from q — the arrows show drive direction, the search runs against them.
Notes: Start with the mission. The cone is everything that feeds the target. VDT answers from a recorded database; we answer live from the simulator’s own interface.

## Slide 3
TWO WAYS TO ANSWER THE SAME QUESTION
VDT Versus the Live VPI Path
 | VDT (Verisium Driver Tracer) | This tool (live VPI)
Data source | Recorded SmartLogWaves.db | The running simulator, during xrun
When it runs | After the simulation finishes | Live, inside the simulation
Prerequisite | Waveform database must exist | None — just -loadvpi the .so
Driver discovery | Comes free from the database | Reconstructed from the design tree
Output | Driver cone + roles + source lines | Driver cone + roles + source lines
Cone on udp-primitive | 40 signals | 39 signals — roles match
39 / 40
signals reproduced against the VDT reference cone
0
waveform databases required
CONTROL / DATA
role labels match VDT exactly
Notes: Same deliverable, two routes. The value is a faster, database-free path — and we validate it against VDT rather than trusting it.

## Slide 4
THE MENTAL MODEL FOR EVERYTHING THAT FOLLOWS
Architecture: Three Phases Around Shared State
PHASE 1
BUILD ONCE
At start of simulation
Walk the design tree
Build signals, driver graph, flop/clock boundaries
Resolve target, compute the cone
Subscribe to two run-time events
PHASE 2
RECORD
Throughout the run
Value-change callback fills the value history
Statement callback records which line wrote what
Hot path: no allocation, O(1) append
PHASE 3
REPORT
At end of simulation
Read the buffers back
Emit JSON for automation
Emit HTML for humans
SHARED STATE — fixed static arrays, written by Phase 1, appended by Phase 2, read by Phase 3
g_signals[]
g_edge_*[]
g_flop_out[]
g_clock_names[]
g_records[]
g_execs[]
g_cone_list[]
VPI is event-driven — you cannot ask for the past. The three-phase shape is forced by how simulators work, not chosen.
Notes: The single most important mental model: build once, record during the run, report at the end. Every function slots into one of these three phases, and the globals are the database.

## Slide 5
THE SPINE OF THE TALK — EVERY LATER SLIDE IS ONE BOX ON THIS MAP
End to End Flow: The Exact Execution Order
ENTRY
PHASE 1
PHASE 2
PHASE 3
vpi_tracer_bootstrap
register_callbacks
subscribes
cbStartOfSimulation
collect_signals_in_scope
detect_flops_in_module
build_driver_graph
find_target_signal
compute_cone
register watches + stmt cbs
value_change_cb
stmt_exec_cb
→ g_records[]
→ g_execs[]
end_of_sim_cb
trace_output.json
report.html
READ IT TOP TO BOTTOM
The simulator loads the library and calls our bootstrap.
The bootstrap registers one start-of-sim callback.
That callback does all setup and subscribes to two events.
Those events fill history during the run.
At the end, history becomes two reports.
Notes: This is the spine. Keep it in mind — every following slide zooms into one box on this map.

## Slide 6
THE HANDSHAKE BETWEEN THE SIMULATOR AND OUR CODE
Entry: Bootstrap and Callback Registration
LOAD .so
START OF SIM
RUN
END OF SIM
register now, run later
vpi_tracer_bootstrap()
The symbol named after the colon on the -loadvpi command line.
All it does is run the startup table.
Keeps the entry point trivial, so real logic lives in normal, testable callbacks.
Without it: the .so loads and nothing ever runs.
register_callbacks()
Subscribes the one callback we can legally register at load time.
memset the callback struct first — stale stack bytes become garbage fields.
reason = cbStartOfSimulation, cb_rtn = start_of_sim_cb.
Without it: setup never runs; the tool does nothing.
Why wait for start-of-sim? At load time the design is not yet elaborated — signals and modules do not exist to query.
Notes: vpi_register_cb is the core subscription primitive: give it an event reason and a function pointer, and the simulator calls you back at that moment.

## Slide 7
START_OF_SIM_CB IS THE CONDUCTOR — NINE ORDERED STEPS, EACH DEPENDING ON THE LAST
Phase 1: The Master Setup Sequence
1
Read the environment
Target, query time, debug, time-gating — configurable without recompiling the .so
2
collect_signals_in_scope
Master inventory of every signal in the hierarchy
3
detect_flops_in_module
Clock names and flop outputs — the stop boundaries
4
build_driver_graph
Reconstruct every driver edge in the design
5
find_target_signal
Resolve the requested signal to a handle and full name
6
compute_cone
Backward BFS — you cannot do this before the graph exists
7
register_cone_watches
You cannot watch cone signals before you know the cone
8
register_stmt_cbs_design
Hook every procedural assignment for writer attribution
9
arm end_of_sim_cb
Registered last, so the report runs after everything is set up
Notes: Nine steps in a fixed order because each depends on the last. Every [TRACER] line in the log is one of these steps announcing itself.

## Slide 8
TWO PASSES THAT EVERYTHING ELSE DEPENDS ON
Signal Inventory and Sequential Boundaries
collect_signals_in_scope()
vpiNet
vpiReg
615 vpiVariables
g_signals[]
de-duplicated by full name
Nets and regs alone MISS SystemVerilog 2-state types — bit, int, byte are invisible to those iterators. Xcelium exposes them under vpiVariables (code 615).
This is exactly the “why is my signal untraceable” bug class.
detect_flops_in_module()
always_ff @(posedge clk)
or @() with posedge / negedge
g_clock_names[]
g_flop_out[]
a
FLOP
q
the cone STOPS here — flop outputs are boundary leaves
Notes: A fan-in trace must stop at flop outputs, otherwise it crosses clock edges and the cone explodes.

## Slide 9
BUILD_DRIVER_GRAPH() — THE INTELLECTUAL CORE OF THE TOOL
Reconstructing Drivers Ourselves
vpi_iterate(vpiDriver) returns NOTHING for behavioural RTL — so the driver graph is something we build, not something we query.
1
Continuous assigns
vpiContAssign → RHS into LHS
2
Procedural blocks
walk every statement tree
3
Guard conditions
if / case / @() → enable, reset, clock
4
Module ports
hop across instance boundaries
5
Gate & UDP primitives
output terminal ← input terminals
add_edge()
g_edge_*[]
dst | src
q | d
q | clk
d | sel
d | bus
sel | rstn
no self-loops · de-duplicated · guard-stamped
Notes: This is where most of the engineering effort went, and the single reason the tool works on real RTL.

## Slide 10
WHERE PROCEDURAL RTL BECOMES GRAPH EDGES
Statement Walking and Expression Cracking
walk_stmt()
Copies the LHS name IMMEDIATELY — vpi_get_str hands back a shared buffer the next call overwrites.
Records blocking vs non-blocking (BA / NBA) for accurate reporting.
The guard stack turns enclosing if / case / @() conditions into edges tagged CONTROL — so enables, resets and clocks appear the way VDT shows them.
if (en) → CONTROL edge
q <= d; → DATA edge
One statement, two different kinds of dependency — both belong in the cone.
collect_rhs_signals() — the expression cracker
=
q
|
&
f( )
b
c
4'd0
d
signals → edges · operators & calls → recurse · part-selects → parent vector · constants → skipped
One recursive descent, reused for right-hand sides, guards AND port connections — which is why those were small additions.
Notes: Assignments are rarely a = b. This recursive descent visits every node type and is reused everywhere, which kept later features small.

## Slide 11
THREE SMALL FUNCTIONS THAT DECIDE WHETHER THE CONE MATCHES VDT
Crossing Boundaries: Edges, Ports and Primitives
collect_port_edges() — hopping a module boundary
parent module
sub-instance
outer_wire
inner_net
vpiHighConn
vpiLowConn
direction decides orientation
collect_primitive_edges() — gate & UDP terminals
clk
rstn
dff_udp
out
vpiPrimTerm → vpiExpr gives the net wired to each terminal
This is how the clock generator traces back to clk and rstn.
add_edge() — the invariant that keeps the graph clean
Skips self-loops
Xcelium sometimes resolves the same handle for both sides
De-duplicates
keeps the cone and report readable
Stamps the branch guard
powers time-gated pruning later
Uses no VPI at all
pure data, so the hot path stays cheap
Notes: The port fix alone took the cone from 2 signals to 11 on the udp-primitive testbench.

## Slide 12
TWO SUPPORTING PASSES BEFORE THE CONE IS COMPUTED
Role Tagging and Target Resolution
add_control_name() — label-only, safe by construction
if (en) / case
g_control_names[]
DATA
CONTROL
Kept in a set SEPARATE from the real clock list, so real-clock semantics stay intact.
Affects the label only — never the cone, the edges, or the values.
Because of that it cannot change results on any other testbench.
find_target_signal() — three ways to resolve a name
Direct lookup
vpi_handle_by_name on the full path
Scan & match
full name, dotted suffix, or leaf name
Bit-select fallback
split sig[N] → vpi_handle_by_index
g_target_full
the seed of the cone
Engineers type whatever is convenient — the resolver makes all three work.
Notes: Role tagging was deliberately scoped to the label so it could not regress any other testbench.

## Slide 13
COMPUTE_CONE() — SIMPLE, BECAUSE THE HARD WORK WAS BUILDING A CORRECT GRAPH
Backward Breadth-First Search With Boundaries
q
d
en
sel
flop_q
LEAF — not expanded
Rings = BFS depth levels, which map straight onto the HTML report tree
THE FOUR RULES
1
Follow edges backward
every edge whose dst is the current node yields a source dependency
2
Stop at flop outputs
added as a leaf, never expanded — we do not cross the clock edge
3
Record cycles
an edge back to the target is logged, not looped forever
4
Skip visited nodes
keeps the search finite and the cone clean
BFS over DFS: it gives natural depth levels.
Notes: Two rules keep it honest — stop at flop outputs, and record cycles instead of looping.

## Slide 14
TWO SUBSCRIPTIONS THAT SET UP EVERYTHING PHASE 2 WILL RECORD
Registering the Run-Time Watches
register_cone_watches()
cbValueChange
on the target, every cone signal, and every clock
Only cone + clocks are watched — watching the whole design would flood the buffer and hit its cap.
A heap-allocated copy of the name rides along in user_data, because it must outlive the registering call.
That is how one shared callback knows WHICH signal fired.
register_stmt_cbs_design()
cbStmt
on every procedural assignment in the design
The recursion must enumerate every container type — begin blocks, if/else, case, loops, fork.
Miss one container and those writes are invisible to writer attribution.
Fires the instant a statement executes, giving file, line and value.
WATCHED
target
cone sig
cone sig
cone sig
clk
✗ everything else in the design — deliberately not watched
Notes: Scoped watching is what keeps the history buffer bounded and relevant.

## Slide 15
DURING THE RUN THE TOOL DOES EXACTLY TWO THINGS — AND BOTH ARE RECORDERS
Phase 2: Two Recorders, One Purpose
value_change_cb() → g_records[]
WHAT a signal became, and WHEN
t=100
0
t=150
1
t=250
1
t=250
0
two changes at ONE tick = a glitch (the delta counter)
stmt_exec_cb() → g_execs[]
WHICH LINE wrote it, and with what value
rtl.sv:41
wrote 0
rtl.sv:58
wrote 1
rtl.sv:72
wrote 0
candidate writers — only one of them actually settled the value
THE JOIN, AT REPORT TIME
rec_value_at(name, tick) → settled value
exec_active_idx(name, tick, value)
the driving line: rtl.sv:58
Match the SETTLED value — picking the last statement instead is the classic bug.
Both are hot paths — fixed arrays, no malloc, O(1) append. They can fire thousands of times without slowing the simulation.
Notes: Two lean streams answering different questions — what vs which-line — cross-referenced only at the end.

## Slide 16
PURE READ-BACK — NO FURTHER VPI QUERIES
Phase 3: Turning History Into Reports
BUFFERS
g_records[]
g_execs[]
g_cone_list[]
g_meta[]
g_edge_*[]
end_of_sim_cb()
fires once — already_called guard
trace_output.json
FOR AUTOMATION
The contract our harness diffs against VDT.
Per signal: value in bin/hex/dec, role, active-writer line, transitions.
Deterministic field order — stable diffs.
report.html
FOR HUMANS
Self-contained — embeds its own CSS and JS, opens anywhere.
Plain-English banner, colour-coded fan-in tree, per-signal timeline cards, live search.
Colours come straight from the SEED / CONTROL / DATA roles.
CRAFTSMANSHIP DETAIL
bin_to_hex and bin_to_dec each own a separate static buffer — sharing one caused a classic aliasing bug.
Notes: Same data, two audiences: JSON for regression automation, HTML for people and reviews.

## Slide 17
EACH STAGE IS ONE EDGE SOURCE SWITCHING ON — UDP-PRIMITIVE TESTBENCH
Proof: Cone Growth From 2 to 39 Against VDT’s 40
Chart: 
| Intra-module only | + Port hops | + Guard edges | + Clock & primitive | VDT reference
Cone size (signals) | 2 | 11 | 29 | 39 | 40
WHAT EACH STEP ADDED
2
Baseline: assigns and processes inside one module only
11
Port hops let the cone cross instance boundaries
29
Guard edges pull in enables, resets and conditions
39
Clock and primitive edges complete the clock leg
40
VDT reference — a one-signal gap, not a missing class of structure
Notes: The staged growth is the clearest evidence that the five edge sources are the right decomposition — each one switched on adds a measurable, explainable jump.

## Slide 18
THREE BIG IDEAS, AND THE DISCIPLINES AROUND THEM
Key Learnings and Design Decisions
1
VPI is event-driven
You cannot ask for the past. The three-phase shape is forced by the platform, not chosen by us.
2
Behavioural RTL has no drivers
vpi_iterate(vpiDriver) is empty — so reconstructing the graph IS the engineering value.
3
Matching VDT means crossing boundaries
Ports, guards, clocks and primitives are exactly what the naive walk stops at.
THE DISCIPLINES THAT COMPOUND
Separate labels from results
CONTROL tagging uses its own set, so it cannot affect any other testbench.
Copy shared buffers at once
vpi_get_str hands back memory the next call overwrites.
Zero every callback struct
Stale stack bytes become garbage fields — and crashes.
Give each helper its own buffer
Shared static buffers caused a real aliasing bug.
Watch only the cone
Bounded, relevant history instead of a flooded buffer.
Static arrays inside a simulator
Predictable memory and no leaks, at the cost of caps.
Notes: Three ideas define the tool. Around them sit small disciplines that individually look minor but together make it reliable inside a live simulator.

## Slide 19
THE WHOLE STORY, END TO END
Complete Summary: One Map, Three Phases
PHASE 1
BUILD ONCE
collect signals
detect flops & clocks
build graph (5 sources)
resolve target
compute cone
watch cone + hook stmts
PHASE 2
RECORD
value_change_cb → g_records[]
stmt_exec_cb → g_execs[]
PHASE 3
REPORT
read the buffers
trace_output.json
report.html
Build the graph once at start · let two callbacks record history during the run · read that history back at the end to explain what drove the target.
Notes: If the audience remembers one sentence, make it the band at the bottom.

## Slide 20
Thank you
A live, database-free reconstruction of VDT’s driver cone — proven by a 39-of-40 signal match with identical role labelling.
39 / 40
signals matched
5
edge sources
0
waveform DBs
Notes: Close on the proof: live, database-free, and validated against VDT rather than trusted.